## Slide 1: CS 3800: Computer Networks Session 1: Introduction
Kalin Zaluzec
Department of Computer Science
Cal Poly Pomona

## Slide 2: Outline of Lecture
Course Information
Introduction

## Slide 3: Course Information
Topics:
  Number representation, integer arithmetic. von Neumann machine. Instruction set architecture. Addressing modes. Assembly programming. Arrays and records. Subroutines and macros. Interrupts. I/O interfacing and communication
Prerequisites:
  C or better in CS 130 or CS 1300 and CS 141 or CS 1400.

## Slide 4: Course Information (Cont’d)
Learning outcomes (at minimum):
  Understand the network architecture design process
  Understand the prominent protocols at various levels in layered protocol design
  Become familiar with recent computer network technologies

## Slide 5: Course Information (Cont’d)
Textbook
  Computer Networking A Top-Down Approach, 8th Edition, by James F Kurose & Keith W. Ross

## Slide 6: Course Information (Cont’d)
Technical Requirements
  Computer with virtualization support
  Virtual box, VMware, etc.
  Python

## Slide 7: Course Information (Cont’d)
Course will roughly cover topics as ordered in the text book
Likely won’t take all semester to get through these topics
  Extra topics added depending on pace of the class

## Slide 8: Course Information (Cont’d)
Canvas
  Syllabus
  Class Notes
    Slides posted day of class
  Assignments
    Posted after class
    Pay attention to due dates
  Posting grades
  Class emails

## Slide 9: Course Information (Cont’d)
Grading Policy:
  Attendance/Participation: 10%
  Homework/Labs: 50%
  Exams: 40% (2 midterms, 1 final, lowest score dropped)
Final letter grades will be based on your overall score as follows (subject to change):
  A ≥ 90
  90 > B+ ≥ 86
  86 > B ≥ 80
  80 > C+ ≥ 76
  76 > C ≥ 70
  70 > D+ ≥ 66
  66 > D ≥ 60
  60 > F

## Slide 10: Course Information (Cont’d)
Late Assignment Policy
  All assignments are expected to be submitted by the specified deadline, but they will (usually) remain open for a week after the deadline)
Honor Code
  All assignments, unless explicitly specified, are to be your own work
  Collaboration is permitted, so long as it is properly documented
  Evidence of cheating, plagiarism, or unauthorized collaboration will result in a 0 grade for quiz/assignment/exam

## Slide 11: Asynchronous class
Mondays
  Mostly lectures
  Occasional collected in-class activities (you will know ahead of time)
  Exams
Wednesdays
  Asynchronous labs
  Pre-recorded lectures

## Slide 12: How to do Well in This Class
Attendance
  Try to attend every class
  Ask questions
Notes
  Take notes and review notes after class
Homework
  Get started early
  Contact me if you encounter problems

## Slide 13: How to Get Help?
Ask questions in class or after class
Attend office hours
Email me
  Put “CS3800” in the subject line
  Send it from your .cpp account
Class Discord (preferred method)
  https://discord.gg/avh2KB4N
  Note: If you direct message me about something important (like missing a class or making up an assignment), include your name!

## Slide 14: Exams
3 exams (lowest score dropped)
  You can skip the final if you do well on both midterms
To be completed during class time
All exams open-notes

## Slide 15: Introductions
Tell us about yourself,
  Name/Year/Major
  Something interesting about yourself
  Expectation in this class
  Optional: Any questions for me?

## Slide 16: Outline of Lecture
Course Information
Introduction

## Slide 17: Internet of Connected Devices
Web-enabled toaster + weather forecaster
Internet phones
Slingbox: remote control cable TV
Security Camera
IP picture frame
Internet refrigerator
Tweet-a-watt: monitor energy use
sensorized, bed mattress
Amazon Echo
Others?
Gaming devices
cars
scooters
bikes
Pacemaker & Monitor
AR devices
Fitbit

## Slide 18: The Internet: A “Nuts and Bolts” View
In
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content provider network
Billions of connected
computing devices:
hosts = end systems
running network apps at
Internet’s “edge”
Communication links
Optical fiber, copper wire , radio, satellite
transmission rate: bandwidth
Packet switches: forward
packets (chunks of data)
  routers, link-layer switches
Networks
collection of devices, routers, links: managed by an organization

## Slide 19: The Internet: A “Nuts and Bolts” View
Internet: “network of networks”
  Interconnected ISPs
protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4/5G, Ethernet
Internet standards
  RFC: Request for Comments
  IETF: Internet Engineering Task
Force
home network
enterprise
network
local or regional ISP
datacenter network
content provider network
Ethernet
HTTP
Skype
IP
WiFi
mobile network
4G
national or global ISP
TCP
Streaming
video

## Slide 20: The Internet: A “Services” View
Infrastructure that provides services to
applications:
  Web, streaming video, multimedia
teleconferencing, email, games, e- commerce, social media, inter- connected appliances, …
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter network
content provider network
HTTP
Skype
Streaming video
provides programming interface
to distributed applications:
  “hooks” allowing sending/receiving apps to “connect” to, use Internet transport service
  provides service options, analogous to postal service

## Slide 21: What is a Protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
Rules for:
… specific messages sent
and
… specific actions taken when message received, or other events
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on message transmission, receipt

## Slide 22: What is a Protocol?
A human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross

## Slide 23: Next Session (also today):
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure

## Slide 24: A closer look at Internet Structure
Network edge:
hosts: clients and servers
servers often in data centers
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content provider network

## Slide 25: A closer look at Internet Structure
mobile network
national or global ISP
local or regional ISP
home network content
provider
network datacenter
network
enterprise
network
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links

## Slide 26: A closer look at Internet Structure
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links
Network core:
interconnected routers
network of networks
mobile network
home network
enterprise
network
national or global ISP
local or regional
ISP
datacenter
network
content provider network

## Slide 27: Access Networks and Physical Media
mobile network
national or global ISP
local or regional ISP
home network content
provider
network datacenter
network
enterprise
network
Q: How to connect end systems to
edge routers?
A: Access Networks
Residential Access Nets
Institutional Access Networks (school, company)
Mobile Access Networks (WiFi, 4G/5G)

## Slide 28: Access Network: Digital Subscriber Line (DSL)
ISP
central office
telephone network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
Use existing telephone line to central office DSLAM
  Data over DSL phone line goes to Internet
  Voice over DSL phone line goes to telephone net
24-52 Mbps dedicated downstream transmission rate
3.5-16 Mbps dedicated upstream transmission rate
DSL
modem
splitter
DSL access multiplexer

## Slide 29: Access Network: Cable-Based Access
cable modem
splitter
…
cable headend
Channels
 |  |  |  |  |  |  |  | C
 |  |  |  |  |  |  |  | O
V | V | V | V | V | V |  |  | N
I | I | I | I | I | I | D | D | T
D | D | D | D | D | D | A | A | R
E | E | E | E | E | E | T | T | O
O | O | O | O | O | O | A | A | L
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
frequency division multiplexing (FDM): different channels transmitted in
different frequency bands
15

## Slide 30: Access Network: Cable-Based Access
cable modem
splitter
…
cable headend
data, TV transmitted at different
frequencies over shared cable
distribution network
HFC: hybrid fiber coax
  asymmetric: up to 40 Mbps – 1.2 Gbps downstream transmission rate, 30-100 Mbps
upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
cable modem termination system
CMTS
ISP

## Slide 31: Wireless Access Networks
Shared wireless access network connects end system to router
via base station aka “access point”
Wireless local area networks
(WLANs)
typically within or around
building (~100 ft)
802.11b/g/n (WiFi): 11, 54, 450
Mbps transmission rate
to Internet
to Internet
Wide-area cellular access networks
provided by mobile, cellular network
operator (10’s km)
10’s Mbps
4G/5G cellular networks

## Slide 32: Access Network: Enterprise Networks
companies, universities, etc.
mix of wired, wireless link technologies, connecting a mix of switches and routers to create a Local Area Network (LAN)
  Ethernet: wired access at 100Mbps, 1Gbps, 10Gbps
  WiFi: wireless access points at 11, 54, 450 Mbps
Ethernet switch
institutional mail, web servers
institutional router
Enterprise link to
ISP (Internet)

## Slide 33: Access Network: Home Networks
to/from headend or
central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (1 Gbps)
WiFi wireless access
point (54, 450 Mbps)
Wireless and wired devices
often combined in single box

## Slide 34: Links: Physical Media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps Ethernet

## Slide 35: Links: Physical Media
Coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple frequency channels on cable
  100’s Mbps per channel
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point
transmission (10’s-100’s Gbps)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise

## Slide 36: Links: Physical Media
Wireless radio
signal carried in various “bands” in electromagnetic spectrum
no physical “wire”
broadcast, “half-duplex”
(sender to receiver)
propagation environment effects:
  reflection
  obstruction by objects
  Interference/noise
Radio link types:
Wireless LAN (WiFi)
  10-100’s Mbps; 10’s of meters
wide-area (e.g., 4G/5G cellular)
  10’s Mbps (4G) over ~10 Km
Bluetooth: cable replacement
  short distances, limited rates
terrestrial microwave
  point-to-point; 45 Mbps channels
satellite
  up to < 100 Mbps (Starlink) downlink
  270 msec end-end delay (geostationary)

## Slide 37: Next Session:
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Layering, Service models
Security

## Slide 38: Lab 1: Virtual Box Setup & Wireshark Intro
Due: Sunday February 2
Assignment remains open a week after deadline
Talk to me if you need more time
Rest of class today: Get virtual box running